## Slide 1
GripSense RGB
Vision-based grip analysis for live camera and offline review.
rejected
background
contact
What it does
Detects whether an object is actually in the hand.
Scores grip using object evidence plus hand posture.
Current focus
V13: reduce false locks on tables and cubicle panels.
YOLO Max offline: stricter object-in-hand scoring.
Live
Offline
Labels
GripSense RGB / 1

## Slide 2
HOW IT WORKS
Grip is not hand closure alone
The system combines hand geometry with detector-backed object evidence before it allows a grip label.
1
Frame capture
Live webcam frames or uploaded video frames are sampled.
2
Hand landmarks
The hand corridor, fingertips, thumb, palm, and closure are estimated.
3
Object evidence
YOLO / RF-DETR evidence proposes non-person object regions.
4
Contact gate
Mask/box overlap, proximity, continuity, and object stability are checked.
5
Grip label
No grip, mild, moderate, or strong is shown only after object-in-hand checks.
GripSense RGB / 2

## Slide 3
OPERATING MODES
One product, three review paths
This extra slide connects the pieces: live demo, offline replay, and exportable batch analysis.
Live V13
Real-time YOLO production mode
Best for demos and immediate feedback. Rejects hand-only and background candidates.
Offline YOLO Max
Upload / process / play / download
Best for inspection. Uses stricter offline scoring and produces annotated MP4/WebM/CSV/JSON.
Future depth mode
RealSense D455 support path
Depth can separate hand, object, table, and background better than RGB alone.
GripSense RGB / 3

## Slide 4
WHERE IT FAILS
Known failure modes
The current algorithm is useful, but it still needs guardrails for hard demo conditions.
Detector flicker
Object appears for one frame, disappears in the next.
Occlusion
The hand hides the object, so the detector thinks it is gone.
Background lock
Tables, cubicle panels, and square wall sections can look object-like.
Fast motion
Motion blur breaks object and hand landmark alignment.
Angle sensitivity
Thin side views of phones/cans are harder to detect.
RGB ambiguity
Without depth, contact is inferred from 2D overlap.
GripSense RGB / 4

## Slide 5
FUTURE ROADMAP
How we make it production-ready
The next improvements should make the model less jumpy, more honest, and easier to verify.
rejected
background
contact
Short-term
V13 gating: reject background panels/tables, smooth visual lock, and decay quickly on real drops.
Offline parity
Make web YOLO Max call the same batch renderer used in the process folder.
Model tuning
Collect object profiles and fine-tune detector classes for demo objects like cans and phones.
Depth upgrade
Use RealSense depth to verify object is between palm/fingers, not behind or on the table.
No object = no grip
Stable lock
Offline review
GripSense RGB / 5